## Slide 1
CoralTwin-DT
Digital Twin of Coral Reefs Under Thermal Stress and Ocean Acidification for Restoration and Conservation Prioritization
Doctoral Research Consortium | Global Change Biology / Ecological Informatics (2026) Scientific Attribution: Resultado obtenido mediante prototipo computacional del gemelo digital

## Slide 2
1. The Global Coral Crisis & Research Motivation
Compounding marine heatwaves and ocean acidification demand dynamic cyber-physical twins
• Mass Bleaching Acceleration: Marine heatwave recurrence has shortened to 5.9 years globally, surpassing the natural decadal recovery window.
• Multi-Stressor Synergy: Atmospheric pCO2 uptake drives ocean acidification, decreasing aragonite saturation and lowering critical thermal tipping points.
• Static Conservation Limitations: Conventional Marine Protected Areas (MPAs) are static and fail to model forward decadal trajectories or prioritize outplanting sites.
• CoralTwin-DT Objective: Engineer an end-to-end 6-layer digital twin coupling satellite telemetry, machine learning, and biophysical ODEs to guide active restoration.

## Slide 3
2. Six-Layer Cyber-Physical Architecture
Unified pipeline from satellite telemetry acquisition to spatial decision support
• Layer 1: Data Acquisition: NOAA Coral Reef Watch (5km), Sentinel-2 MSI (10m), Allen Coral Atlas, In-situ Moorings.
• Layer 2: Data Integration: 500m x 500m grid resampling, daily aggregation, ISO 19115 FAIR metadata catalog.
• Layer 3: Hybrid Modeling: Coupled XGBoost / RF / Deep MLP classifiers and Mumby non-linear dynamical ODEs.
• Layer 4: Scenario Simulation: Forward 2025-2050 projections across SSP5-8.5, SSP2-4.5, Outplanting, and MPA protection.
• Layer 5: Model Validation: 5-Fold Spatially Stratified CV, backtesting (2016-2024), and N=5,000 Monte Carlo uncertainty bounds.
• Layer 6: Decision Support: Interactive Environmental Dashboard and Spatial Restoration Priority Index (SRPI) Cartography.

## Slide 4
3. Machine Learning Performance (5-Fold Spatial CV)
XGBoost achieves state-of-the-art classification and regression accuracy
• XGBoost Multi-Task Accuracy: Macro-F1 = 0.958, Accuracy = 96.1%, R² = 0.934 (RMSE = 3.82% cover loss).
• Random Forest Performance: Macro-F1 = 0.942, Accuracy = 94.6%, R² = 0.918 (RMSE = 4.25%).
• Deep MLP Neural Network: Macro-F1 = 0.915, Accuracy = 91.9%, R² = 0.885 (RMSE = 5.08%).
• Linear Baseline Contrast: Logistic / Ridge baseline achieves only Macro-F1 = 0.782, demonstrating critical non-linearity.
• Spatial Generalization: Spatial block cross-validation confirms high out-of-fold generalization with zero spatial leakage.

## Slide 5
4. TreeSHAP Explainability & Tipping Point Discovery
Quantifying the exact marginal contribution of compounding oceanographic stressors
• Dominant Feature Contribution: Degree Heating Weeks (DHW) drives 38.4% of total predictive variance.
• Carbonate System Impairment: Aragonite saturation (21.2%) and seawater pH (14.8%) represent secondary critical controls.
• Structural Resilience: Benthic rugosity (11.5%) and optical turbidity (6.9%) provide significant localized buffering.
• Synergistic Tipping Point: Under acidified conditions (pH 7.75, Omega 2.45), the thermal mortality threshold drops from 8.5 to 5.8 °C-weeks.

## Slide 6
5. Forward Scenario Trajectories (2025–2050)
Coupled dynamical simulations evaluate intervention trade-offs under IPCC pathways
• Scenario 1 (SSP5-8.5 Unmitigated): Coral cover collapses to 4.8% by 2050; net framework dissolution (-1.82 kg CaCO3/m²/yr).
• Scenario 2 (SSP2-4.5 Moderate): Coral cover stabilizes at 21.4% with modest framework accretion (+2.45 kg CaCO3/m²/yr).
• Scenario 3 (Active Outplanting): Thermally resilient micro-fragments (+2°C tolerance) maintain 38.7% cover and +5.10 kg CaCO3/m²/yr.
• Scenario 4 (Integrated MPA + Outplant): Synergistic recovery to 46.2% live coral cover and +6.80 kg CaCO3/m²/yr framework growth.

## Slide 7
6. Spatial Restoration Priority Index (SRPI)
Multi-criteria spatial decision analysis channels outplanting into hydrodynamic micro-refugia
• Multi-Criteria Formulation: Integrates Thermal Refugia (35%), Degradation Urgency (25%), Rugosity (25%), and Water Clarity (15%).
• Tier 1 Action Zones: Top 25% priority parcels identified in well-flushed fore-reef sectors with high structural complexity.
• Open GIS Vector Delivery: Standard GeoJSON priority zoning layer enables seamless ingestion into QGIS, ArcGIS, and marine park portals.

## Slide 8
7. Conclusions & Management Policy Recommendations
Evidence-based digital twins for 21st century marine conservation
• Digital Twins Bridge the Gap: Coupling satellite remote sensing with AI and dynamical biophysics unlocks proactive reef management.
• Acidification Cannot Be Ignored: Operational marine heatwave alert systems must incorporate carbonate saturation modifiers.
• Hybrid Conservation Mandate: Resource managers must combine no-take MPA herbivory protection with active resilient micro-fragment propagation.
• FAIR Open-Source Release: Complete repository, models, and data are publicly available at https://github.com/HrSly11/CoralTwin-DT.git